Minutes of Meeting
GMRT

Minutes of Meeting

Meeting	Meeting related to In House CMS development
Held on	14-Aug-2012; Time : 3.30 PM to 5.30 PM; GMRT user's room
Attendees	Nimisha, Jitendra, Raju, Santaji and Naresh
Agenda	In House CMS development
Highlights / and items / discussed	Discussed following items : / Naresh explained about old MCM card and New rabbit card. / Rabbit has USB/Serial interface for programming. / Rabbit will be programmed using dynamic C and it support multitasking. / Rabbit 4300 has 512 KB of RAM and separate 512 KB flash memory. / Rabbit support 2 GB of SD memory. Rabbit memory has more than enough / memory for it'd operation. / Old MCM has 16 control channel and Rabbit has 32 control channel. / New MCM support 2 SPI port for Analog system. / LO monitoring requires some searching for frequency to voltage conversion. / Old MCM is used by baseband system for 4th LO. / New MCM is used for GPU correlator. / CEB 0 used to reset all ABCs. / Old MCM supports only serial, New MCM supports Serial/Ethernet. / Rabbit processor supports floating point calculations and has RTC. / Old MCM has to get commands in a proper protocol. / New MCM can accept ASCII based commands from New Online. / Raju explained about various work done on TELESET-ABCCOM software chain. / We have to get input from Charu regarding Rabbit Old MCM program testing / with antenna sub-systems. / Existing Online follow Client/Server model for interaction with DAS chain. / Online send ASCII based command to DAS system. / We should build system in such a way that it should run 20 years.