Work Report ( period 1.10.2013 to 31.10.2013) by RRU
    1. Tested setting control bit by connecting test jig in C03 antenna test set up with the help of MBM by both GUI & terminal input.
    2. Explored Ethernet broadcast & circulated document.
    3. Implemented state machine logic in Online_v2 where Online_v2 will not crashed by any malfunctioning at antenna side like power shutdown, cable unplugging, ERROR in reading MCM response. Whenever Online_v2 detects any of these, it kill that particular antenna device thread by calling terminate_thread function. All this test condition tested in Lab as well as C03 antenna. Implemented the terminate_thread function in Online_v2 which takes care of terminating the thread.
    4. Generated plots for experiment using GNU plot.
      plotted various data point like
      1. Time between command & response
      2. Time between two successive monitoring packets.
    5. Done the modification in mcmtest.c program as per FE group request.
    6. Reconfigured whole Lab network setup for Online_v2 development including teleset machine, incms machine, N/W switch.
      After N/W reconfiguration 1 second back ground monitoring has been working fine .
    7. Performed GCC duty as per GCC schedule.